## Slide 1: CITS 5506 The Internet of Things Group 25 Trash Talk: Exploring City Waste Management and Smart Bin Technology

## Slide 2
Trash Talk: Exploring City Waste Management and Smart Bin Technology
Team members' names and Student Numbers:
  Han Sun (23913189)
  Tom Nguyen (22914578)
  Koid Xian Ting (24292249)
  Difu Xiao (24473616)
  Steven Li (24291799)
Department of Engineering and Mathematical Sciences
15/10/2024
Project and Team

## Slide 3
Traditional Waste collection
Unpredictable waste generation: Bins are emptied on fixed schedules, regardless of whether they're full or not.
Manual inspections: Waste collection teams must physically check each bin to see if it's full, leading to inefficient use of time and resources.
Inefficient use of resources: Trucks drive the same routes even when some bins are nearly empty, wasting fuel and labour.
Increased operational costs: The combination of unnecessary trips, manual checks, and rigid schedules adds to the overall cost of waste management.
Problem statement (Why)

## Slide 4
Traditional Waste collection
Unpredictable waste generation: Bins are emptied on fixed schedules, regardless of whether they're full or not.
Manual inspections: Waste collection teams must physically check each bin to see if it's full, leading to inefficient use of time and resources.
Inefficient use of resources: Trucks drive the same routes even when some bins are nearly empty, wasting fuel and labour.
Increased operational costs: The combination of unnecessary trips, manual checks, and rigid schedules adds to the overall cost of waste management.
Problem statement (Why)

## Slide 5
Traditional Waste collection
Unpredictable waste generation: Bins are emptied on fixed schedules, regardless of whether they're full or not.
Manual inspections: Waste collection teams must physically check each bin to see if it's full, leading to inefficient use of time and resources.
Inefficient use of resources: Trucks drive the same routes even when some bins are nearly empty, wasting fuel and labour.
Increased operational costs: The combination of unnecessary trips, manual checks, and rigid schedules adds to the overall cost of waste management.
Problem statement (Why)

## Slide 6
Traditional Waste collection
Unpredictable waste generation: Bins are emptied on fixed schedules, regardless of whether they're full or not.
Manual inspections: Waste collection teams must physically check each bin to see if it's full, leading to inefficient use of time and resources.
Inefficient use of resources: Trucks drive the same routes even when some bins are nearly empty, wasting fuel and labour.
Increased operational costs: The combination of unnecessary trips, manual checks, and rigid schedules adds to the overall cost of waste management.
Problem statement (Why)

## Slide 7
Aim of the Trash Talk System
Develop a complete smart trash bin system that integrates backend, cloud infrastructure, frontend, and IoT devices with sensors.
Make waste collection more efficient and cost-effective.
Improve cleanliness, safety, and sustainability in public areas.
Offer real-time updates on bin fill levels, locations, and temperature.
Objectives of the project (What)

## Slide 8
Aim of the Trash Talk System
Develop a complete smart trash bin system that integrates backend, cloud infrastructure, frontend, and IoT devices with sensors.
Make waste collection more efficient and cost-effective.
Improve cleanliness, safety, and sustainability in public areas.
Offer real-time updates on bin fill levels, locations, and temperature.
Objectives of the project (What)

## Slide 9
Aim of the Trash Talk System
Develop a complete smart trash bin system that integrates backend, cloud infrastructure, frontend, and IoT devices with sensors.
Make waste collection more efficient and cost-effective.
Improve cleanliness, safety, and sustainability in public areas.
Offer real-time updates on bin fill levels, locations, and temperature.
Objectives of the project (What)

## Slide 10
Aim of the Trash Talk System
Develop a complete smart trash bin system that integrates backend, cloud infrastructure, frontend, and IoT devices with sensors.
Make waste collection more efficient and cost-effective.
Improve cleanliness, safety, and sustainability in public areas.
Offer real-time updates on bin fill levels, locations, and temperature.
Objectives of the project (What)

## Slide 11
Perth Smart Cities Initiative
  Ultrasonic sensor to calculate the bin levels
  Bin Temperature
  Battery Power
  Lid Tilt / Openings
  LoRaWAN
How the project builds on or differs from existing solutions:
  An end-to-end system built with system modularity in mind.
  Focuses on integrating with smart city infrastructure.
Literature Review

## Slide 12
1. Hardware Subsystem
2. Communication Subsystem
3. Software Subsystem
4. User Interface / Dashboard Subsystem
5. Cloud Infrastructure
System Overview

## Slide 13
Project Description (How)

## Slide 14
Divide and Conquer:
Hardware Team
  Han, Difu
Software Team
  Tom, Steven
Data Analytics Team
  Koid
Methodology (How)

## Slide 15
  System Design / Architecture
  Prototyping
  Software Testing
  Software Optimization / Sensor Calibration
  Data Analyses / UI / Dashboard
Design and Development Process

## Slide 16
System Architectures
Hardware Subsystem
Event Driven Architecture
​
Software Subsystem
TCP/IP
MQTT Protocol
PUB/SUB Topology
Client Server Architecture

## Slide 17
Technologies used to develop the Hardware
Ultrasonic sensor
Temperature sensor
GPS module
Wi-Fi communication
Tilt Sensor
LoRa
Arduino IDE
Hardware Subsystem

## Slide 18
Hardware Subsystem
Event Driven Architecture​
​

## Slide 19
Hardware Subsystem

## Slide 20
Hardware Subsystem (Arduino)

## Slide 21
Hardware Subsystem (mosquitto)

## Slide 22
Price of the components:
  Ultrasonic Sensor: $7.95
  Temperature Sensor: $4.00
  TTGO T-Beam v1.2 ESP32: $54.19
  AA Battery: $4.55
  Jumper wires: $5.20
  USB Cable: $5.70
  TTGO T-Beam v1.0 Breadboard adapter: $45.00
  8. Tilt sensor: $4.55
Total cost of the prototype: $131.14
Cost

## Slide 23
Software Subsystem
PUB/SUB Topology

## Slide 24
Technologies used in the software subsystem
C
Python
  Paho for Python MQTT communication
  Flask for web services
  SQLAlchemy ORM as cross-platform solution
SQL (initially implemented with python DBAPI and SQL )
Unit tests (unittest and automated github actions)
Mosquitto utilities for MQTT pub/sub testing
Shell for application deployment.
Software Subsystem

## Slide 25
Cloud Services used:
TTN for MQTT server
  https://au1.cloud.thethings.network/console/applications/smart-bin-mqtt-server/
Mosquitto for MQTT testing server
  https://test.mosquitto.org/
Github for coding CR
  https://github.com/steven-app/smartbin
AWS for database services
  PostgreSQL
  Metabase for interactive dashboard
  https://www.metabase.com/
Render for application deployment
  https://dashboard.render.com/
Uptime for monitoring webservice availability
  https://uptime.com/
Cloud Services

## Slide 26
The Things Network Console

## Slide 27
Backend Console
Base64 Encoded JSON
Plain Text

## Slide 28
PostgreSQL

## Slide 29
Ensuring long-term power supply for sensors:
  AA battery capacity is too low.
  Used a high-capacity power bank
Reliable LoRa Communication:
  Unable to reliably connect to LoRaWAN
  WiFi was used as a back up if LoRaWAN was unavailable.
Cloud Infrastructure Pricing:
  AWS can be expensive.
  Used AWS Free Tier.
Key challenges and solutions

## Slide 30
How does the result address the problem statement?
    Improved waste management efficiency
    Enhanced public space cleanliness
    Cost savings
Unexpected issues:
    Underestimated the time constraint (6 weeks) and complexity of Lora technology
    Availability of LoRaWAN (not available at home)
    Not enough meaningful data from our own smart bin system
Results and Discussion
Notes: By having this system
Management team can plan the garbage collection route and time schedule based on previous data and current fill level of the bins.
2. By improving the efficiency of garbage collection, we can prevent bin overflow.
3. Save both labor & fuel cost.
Unable to connect to the Lora gateway at home, can only connect in UWA.

## Slide 31
Dashboard Results
Location of 10 smart bins in UWA (GPS sensor)
Fill Level Overview of 10 bins
(Ultrasonic sensor)
Metabase dashboard built using Mock Data and real-world data from City of Melbourne
Notes: Users can find and access the smart bins in UWA. (gps sensor)
(ultrasonic sensor) 80% is the critical fill level of the fill level percentage which needs to be emptied immediately.
Two bins are nearly full, which requires immediate collection.

## Slide 32
Dashboard Results
Overview of Real-Time Bin Status
Normal – Green
Anomalies - Red
Notes: Real Time Bin Status Overview (temperature, tilt, communication & displacement status)
Normal status is coded in green color.
Status anomalies is coded in red color
Bin ID 2 displaced and Bin ID 6 is tilted.

## Slide 33
Dashboard Results
Garbage Collection Frequency for:
Efficient garbage collection route planning
Flags for bins that have not been emptied for more than seven days
Notes: ---- We considered the garbage is being collected after fill Level drops below more than 30% of its previous fill level. The average collection time & days since last emptied are being calculated automatically based on the logic of algorithm.
Left: Average Collection Time (Days) -efficient garbage collection
Right:
Sends an email to the stakeholders (needs attention). Attract rodents and produce bad smells if organic matters have been left unattended for more than 7 days.

## Slide 34
Dashboard Results
Notes: We've got the real world data from the city of Melbourne local government.
The fill level fluctuates regularly, with some bins filling up faster than others like bin 6 and 7..

## Slide 35
Dashboard Results
Summary of Key Metrics
Allow for quick decisions and actions
Notes: Put on top of the dashboard ---> easy for management team to have a quick overview of the current key status of the system in order to make quick actions and decisions.
For example : clean the bins, straighten the tilted bins and reposition displaced bins.

## Slide 36
Summary of the project outcomes:
  Successfully developed an end-to-end smart trash bin system
  Real-time waste management monitoring
  Demonstrated potential for improving urban cleanliness and efficiency
Lessons learned:
  Importance of testing and validating sensor accuracy
  Underestimated LoRaWAN complexity
  Communication and well-defined responsibilities were important to successfully deliver the project and its subsystems.
Potential for future work or improvements:
  Expansion to include waste sorting capabilities
  Implementation of machine learning for predictive waste generation
  Algorithm based routing and scheduling
Conclusion

## Slide 37
?
Q&A Slide

## Slide 38
Demo

## Slide 39
Technovation, "Smart Garbage Monitoring System Using Internet of Things (IOT)"
CleanRobotics, "Smart Waste Management: Why Smart Bins are the Future of Recycling"
RTS, "What are Smart Waste Bins and How are They Changing Recycling?"
City of Perth, "Smart Cities"
PRNewswire, "City of Sydney to Deploy SmartBin™ and Revolutionise Waste Collections"
STREETS DEPARTMENT, "Review of Streets Department Bigbelly Operations"
IJCRT, "A Review of IoT Based Intelligent Bins & Smart Waste Management Systems"
Gatti et al., "Toward Greener Smart Cities: A Critical Review of Classic and Machine-Learning-Based Algorithms for Smart Bin Collection"
Metabase, "Metabase: An open-source business intelligence tool"
Amazon Web Services, Inc., "Amazon Web Services (AWS) - Cloud Computing Services"
The Things Network, "The Things Network - Global open LoRaWAN network"
References